QUIZ

"DOT CARGO SECUREMENT"

PRESENTER'S COPY...WITH ANSWERS

1.	True or False?... GVWR is an acronym for "Gross Vehicle Weight Rating".

X   	True		       	False

2.	True or False?... In general terms, the Standard requires all types of cargo to meet one of three conditions in order to be transported securely.

X   	True		       	False

3.	True or False?... "Vehicle structures" that can be used in securing cargo include floors, walls, decks, headboards, bulkheads, anchor points, stakes and posts.

X   	True		      	False

4.	True or False?... Whether you're transporting stacks of lumber, rolls of newsprint, packaged electronic equipment or a combination of materials, each load you carry has the same characteristics that will have to be addressed by the securement system that restrains it.

True		   X   	False

5.	True or False?... A "Gross Vehicle Weight Rating" is marked on the inside door jam on the driver's side of a truck's cab.

X   	True		      	False

6.	True or False?... A securement system must be able to withstand a minimum amount of force in only three directions… forward, rearward and sideways.

True		   X    	False

7.	True or False?… "Securing Devices" are devices that have been specially manufactured to attach and secure cargo to a truck or trailer.

X   	True		      	False

8.	True or False?... "Curb weight" is what a vehicle weighs with passengers and cargo in it.

True		   X   	False

9.	True or False?... "WLL" stands for "Working Load Limit".

X   	True		       	False

10.	True or False?... The DOT Cargo Securement Standard states that any type of cargo that you load onto a truck or trailer should be positioned on the vehicle to avoid overloading any one of its axles.

X   	True		       	False

RCK-398