QUIZ

"MANUAL PALLET JACK SAFETY"

PRESENTER'S COPY...WITH ANSWERS

1.	True or False?... Pallet jacks are designed to be used on surfaces that are smooth, dry and level.

X   	True		       	False

2.	True or False?... To lower the forks of a pallet jack, you push the actuating lever to the "down" position.

True		   X   	False

3.	True or False?... As long as you park a pallet jack on a level surface, it is safe to leave the equipment unattended with its forks raised.

True		   X   	False

4.	True or False?... You should always use safe work practices and follow the "rules of the road" when you operate a pallet jack.

X   	True		       	False

5.	True or False?... When you are raising the forks of a pallet jack you should use both arms to pump the tiller.

X   	True		       	False

6.	True or False?... Since loading docks tend to be crowded, it is okay to operate a pallet jack close to the edge of a dock if you are careful.

True		   X   	False

7.	True or False?… When you are operating a pallet jack on an incline, traveling at an angle or trying to turn the equipment can often lead to a tipover.

X   	True		       	False

8.	True or False?... Pulling a pallet jack out of a truck onto a lift gate is the safest way to get it out of the truck.

True		   X   	False

9.	True or False?... It is safe to assume that dock plates and levelers will be strong enough to support the weight of any pallet jack and the load that it is carrying.

True		   X   	False

10.	True or False?... You should always stay uphill of a pallet jack on an incline so you don't get run over by the equipment if it gets out of control.

X   	True		       	False

SMK-349